8085 Instruction Types & Execution
8085 Instruction Types & Execution

---
8085 - Instruction Word Size
8085 - Instruction Word Size
1 Byte ------------- MOV C,A	0100 1111	4F
ADD B	1000 0000	80
CMA	0010 1111	2F
(occupies 1 memory location)
_________________________________________________________________________________________
2 Byte -------------- MVI A,32H	0011 1110	3E
        0011 0010	32
(occupies 2 memory location, operation code & operand in 8 bit)
__________________________________________________________________________________________
3 Byte	------------- LDA 2050H	0011 1010	3A
0101 0000	50
0010 0000	20
(occupies 3 memory locations, opcode & operand in 16 bit)

---
1 byte instruction – A mnemonic followed by a letter or two letters
MOV A,B
RRC
2 byte instruction – A mnemonic followed by 8 bit operand
MVI A, 00H
3 byte instruction - A mnemonic followed by 16 bit operand
LXI B, 16bit
CALL 16bitaddress

---
Opcode Format
Opcode Format
Code	Registers
000	B
001	C
010	D
011	E
100	H
101	L
111	A
110	Memory related operations
00	BC
01	DE
10	HL
11	SP
 1.Rotate each bit of the accumulator to the left by 1
00000 111	07H (8bit opcode)
2.Add the contents of a register to Accumulator
 ADD B
10000 000	80H
3. Move the contents from Rs to Rd
MOV C,A
01 001 111	4F

---
Opcodes for instructions
Opcodes for instructions
MOV A,32H	3E
32
   MVI B,48H	06
48
    ADD B	80
    OUT 01H	D3
01
    HLT	76

---
Program stored in Memory
Program stored in Memory
  Mnemonics	Hexcode	Binarycode Mem_addr
MOV A,32H	3E	00111110	2000
32	00110010	2001
   MVI B,48H	06	00000110	2002
48	01001000	2003
    ADD B	80	10000000	2004
    OUT 01H	D3	11010011	2005
01	00000001	2006
    HLT	76	01111110	2007

---
Addressing Modes - 8085
Addressing Modes - 8085
- Direct Addressing: In this mode, the operand is specified within the instruction itself . (Eg) LDA 4000H; STA 5513H
- Register Addressing: In this mode of addressing, the operand are in the general purpose registers. (eg) MOV A, B ; ADD D
- Register Indirect Addressing: MOV A, M; ADD M . These instructions utilise 1-byte. In this mode, instead of specifying a register, a register pair is specified to accommodate the 16-bit address of the operand
- Immediate Addressing: MVI A, 07; ADI 0F are examples of Immediate Addressing mode. The operand is specified in the instruction in this mode.
- Implicit Addressing: In this mode of addressing, the operand is fully absent. Examples are RAR, RAL, CMA, etc.

---
Timing & Control
Timing & Control
- The Timing & Contrl section is a part of CPU and generates timing and control signals for execution of instructions.
- This section includes Clock signals, Control signals, Status signals, DMA signals as also the Reset section.
- It controls fetching and decoding operations.
- It also generates appropriate control signals for instruction execution as also the signals required to interface external devices.

---
Timing Diagram
Timing Diagram
- A time diagram is a graphical representation.
- The 8085 instruction timing diagram represents the execution time of each instruction in graphical format.
- Execution time is given in T-states.
- The 8085 microprocessor has a set of control signals and data signals that play an important role in the execution of instructions.

---
Signals
Signals
- Clock Signal: The time required to execute an instruction is called a clock cycle.
- Machine Cycle: The time required to access memory or input/output devices is called a machine cycle. The 8085 has 5 basic machine cycles i.e., load opcode, read from memory, write to memory, read I/O, and write I/O.
- T-State: A machine cycle and an instruction cycle take several clock periods. The portion of an operation performed in one system clock period is called a T-state.
- Control Signals: The control signal controls the operations. Common signals are ALE (address block enable), RD (read), WR (write), and IO/M (input/output) memory.

---
Control Signals
Control Signals
- IO/ M signal indicates whether I/O or memory operation is being carried out. A high on this signal indicates I/O operation while a low indicates memory operation.
- S0 and S1 indicate the type of machine cycle in progress

---
ALE
ALE
- ALE pin which stands for ‘Address Latch Enable’.
- ALE signal is used to demultiplex the lower order address bus (AD0 – AD7).
- Pins 12 to 19 of 8085 are AD0 – AD7 which is the multiplexed address-data bus. Multiplexing is done to reduce the number of pins of 8085
- ALE signal goes high at the beginning of T1 of each machine cycle and goes low at the end of T1 and remains low during the rest of the machine cycle.
- This high to low transition of ALE signal at the end of T1 is used to latch the lower order address byte (A0 – A7) by the latch IC 74LS373, so that the lower byte A0 – A7 is continued to be available till the end of the machine cycle.

---
Read/Write
Read/Write
- Data transfer from memory or I/O device to microprocessor or the reverse takes place during T2 and T3 states of the machine cycles.
- In the read machine cycle, data appears at the beginning of T3 state, whereas in the write machine cycle, it appears at the beginning of T2

---
8085 Machine Cycles
8085 Machine Cycles
The 8085 microprocessor has 5 basic machine cycles.
- Opcode Fetch {4T- state}
- Memory Read {3T- state}
- Memory Write {3T- state}
- I/O Read {3T- state}
- I/O Write {3T- state}

---
Opcode Fetch Machine Cycle of 8085
Opcode Fetch Machine Cycle of 8085
- Each processor instruction has a one byte opcode.
- Operation codes are stored in memory. Thus, the processor performs an opcode load machine cycle to load the opcode from memory.
- Thus, each instruction begins with a machine cycle of opcodes.
- The time the processor takes to perform an opcode load cycle is 4T.
- At this time, the first, 3T-states are used to load the opcode from memory, and the remaining T-states are used for internal opcodes.

---
- The first machine cycle of every instruction is the Opcode Fetch.
- The length of this machine cycle varies between 4T to 6T states—it depends on the type of instruction.
- The processor places the contents of the PC on the address lines, identifies the nature of machine cycle æ (by IO/M, S0, S1) and activates the ALE signal. All these occur in T1 state.
- In T2 state, RD signal is activated so that the identified memory location is read from and places the content on the data bus (D0 – D7).
- In T3, data on the data bus is put into the instruction register (IR) and also raises ææ the RD signal thereby disabling the memory.
- In T4, the processor takes the decision, on the basis of decoding the IR, whether to enter into T5 and T6 or to enter T1 of the next machine cycle

---
The lower byte of address (AD0 – AD7) is available on the multiplexed address/data bus during T1 state of each machine cycle, except during the bus idle machine cycle.
The higher byte of address (A8 – A15) is available during T1 to T3 states of each machine cycle, except during the bus idle machine cycle

---
Memory R/W
Memory R/W
- Both the Memory Read and Memory Write machine cycles are 3T states in length.
- In Memory Read the contents of R/W memory (including stack also) or ROM are read while in Memory Write, it stores data into data memory (including stack memory).
- During T2 and T3 states data from either memory or CPU are made available in Memory Read or Memory Write machine cycles respectively.
- The status signal (IO/ M, S0, S1) states are complementary in nature in Memory Read and Memory Write cycles.
- Reading or writing operations are performed in T2.
- In T3 of Memory Read, data from data bus are placed into the specified register and raises RD so that memory is disabled while in T3 of Memory Write WR signal is raised which disables the memory.

---
I/O R & W
I/O R & W
- I/O Read and Write machine cycles are almost similar to Memory Read and Write machine cycles respectively.
- The difference is in the IO/ M signal status which remains 1 indicating that these machine cycles are related to I/O operations.
- These machine cycles take 3T states.
- In I/O read, data are available in T2 and T3 states, while during the same time (T2 and T3) data from CPU are made available in I/O write.

---
Timing Diagram of MOV A,B
Timing Diagram of MOV A,B
- Since the program counter sequences the execution of instructions, it is assumed that the PC holds the address 4080H AND accumumlator having the content FFH.
- While the system executes the instruction, the following takes place one after another.
1. The CPU places the address 4080H (residing in PC) on the address bus—40H on the high order bus A15 – A8 and 80H on the low order bus AD7 – AD0.
2. The CPU raises the ALE signal to go high— the H to L transition of ALE at the end of the first T state demultiplexes the low order bus.
3. The CPU identifies the nature of the machine cycle by means of the three status signals IO/ M, S0 and S1. IO/ = 0, S1 = 1, S0 = 1
4. In T2, memory is enabled by the signal. The content of PC i.e., 47H is placed on the data bus. PC is incremented to 4081H.
5. In T3, CPU reads 47H and places it in the instruction register.
6. In T4, CPU decodes the instruction, places FFH (accumulator content) in the temporary register and then transfers it to register B. It consists of 4T states

---
Timing Diagram of MVI A,45H
Timing Diagram of MVI A,45H
- Loading opcode 4EH from memory 2000H. (Operation Code Loading Machine Cycle)
- Read (move) data 45H from memory 2001H. (memory reading).

---
Timing Diagram of STA 8000H
Timing Diagram of STA 8000H
- STA stands for Store Accumulator – the contents of the accumulator are stored at (1000H).
- The transaction code of STA indicates 32H.
- It is provided by 1000H memory (assumed) – In the machine cycle.
- Then read the sub address (00). – Memory reading machine cycle
- Read higher memory location (80) – Memory read machine cycle.
- Consider the combination of the two addresses and write the details of the accumulator for 8000.
- Assume the memory address for the instruction and let the content of accumulator is C7H.
- So, C7H from accumulator is now stored in 8000H.